## Slide 1
Project Goals
Design a radar sensor
  start with a standard use case (see below) and/or an idea of your own
  document your HW/DSP-concept
Realize your prototype
  Hardware
  Firmware/Software
Test the performance of your prototype
Document and present your prototype
PM4 FS2026: CW-Doppler-Radar Sensor
v
radial velocity
range R
radar sensor
K-LC5
radar sensor
K-LC5

## Slide 2
References
General information can be simply found on Wikipedia:
  Distance and Spead Measurement, Radar Range Equation, …
Further technical information can be found on the Radar Tutorial:
  Doppler-Effect (see Figure 1 first)
  CW-Doppler-Radar (only sections Doppler Radar, Function, Block diagram of CW radar Figure 3)
  Radar Range Equation
  Radar-Cross-Section
RFbeam, St. Gallen: https://www.rfbeam.ch/
  use cases
  Radar sensor used in PM4:
    Radar Sensor K-LC5 , data sheet K-LC5

## Slide 3
1. CW-Doppler-Radar: motion sensor
- for movement detection
- indoor automation
- intrusion alarm
challenge: human presence detection
2. CW-Doppler-Radar: speed sensor
- traffic monitoring
- sports (challenge: reflectivity of target)
3. FMCW-Radar: range sensor - please see corresponding document
- range (i.e. distance) measurements
- more challenging than CW-Doppler-Radar
Some use cases
use case 2
use case 1
use case 1
Source: https://rfbeam.ch/applications/

## Slide 4
v
radial velocity
range R
= fc
(in-phase signal) I(t) = A·cos(2π·fd·t-φ0)
=> I(t) = y(t)·cos(2π·fc·t) low-pass filtered
x(t) = cos(2π·fc·t)
VCO: voltage controlled oscillator
LNA: Low Noise Amplifier
CW-Doppler-Radar: DC to set fc (should be different to avoid interference between sensors)
FMCW-Radar: sawtooth (DAC with reconstruction filter)
y(t) = A·cos(2π·(fc+fd)·t)
Doppler-Effect
Doppler-frequency
wave length λ
c: speed of light (~ 3·108 m/s)
fc: transmit frequency ( 24 GHz)
v / (m/s) | v / (km/h) | fd / Hz
0.1 | 0.36 | 16
0.28 | 1 | 44.4
1 | 3.6 | 160
2.8 | 10 | 444
10 | 36 | 1600
28 | 100 | 4444
CW-Doppler-Radar: How it works
(quadrature-phase signal) Q(t) = A·sin(2π·fd·t-φ0)
=> Q(t) = y(t)·(-sin(2π·fc·t)) low-pass filtered
CW-Doppler-Radar
cos(2π·fc·t)
target

## Slide 5
Review of Fourier Theory
multiplication with ej2πfc·t ○-● frequency translation with +fc (to the right)
x(t) = y(t) · ej2πfc·t ○-● X(f) = Y(f-fc)
Frequency translation
cos(ωc·t) = (ej·ωc·t + e-j·ωc·t) / 2
Euler-formula:
Multiplication of the received signal y(t) with cos(2π·fc·t) causes a frequency translation by ±fc (see the following spectra)
IY(f)I
fc
fc
f
f
-fc
-fc
+fc
+fc
fDoppler
X
X
filtered
II(f)I
fc - fDoppler
target moves away from the radar sensor (v<0) and causes a negative Doppler frequency

## Slide 6
Exercise 1
Assume that the target moves towards the radar sensor (v>0) and, thus, causes a positive Doppler frequency (fd>0)
In the following diagram, sketch the magnitude spectra
IY(f)I of the reflected radar signal y(t) and
II(f)I of the analog radar-sensor output signal I(t)
Please verify that the sign of the Doppler frequency fd and the velocity v and, hence, the direction of the movement can not be distinguished if only 1 sensor output signal is used !
IY(f)I
fc
fc
f
f
fd
II(f)I

## Slide 7
FFT-based Doppler frequency detection
Review of FFT
fc
f
fd
X
X
filtered
II(f)I
fs
f
fs-fd
fs/2
fd
The FFT transforms N samples in the time-period [0,…,NTs) into N uniformly distributed (complex) spectral-values in the range [0,…,fs).
II[m]I
Spectrum of analog radar sensor output signal I(t)
FFT-spectrum of the sampled radar sensor output signal I[n] = I(t=nTs)
(fs is the sampling frequency)
f
-fd
fd
Zero-frequency component shifted to
center of spectrum (Matlab: fftshift)
fs/2
FFT
fftshift

## Slide 8
Determination of movement direction
Multiplication with e-j2πfc·t ○-● frequency translation with -fc (to the left)
IY(f)I
fc
f
-fc
fc
f
-fd
X
filtered
y(t)·e-j2πfc·t = y(t)·[ cos(2πfc·t) - j·sin(2πfc·t) ] = I(t) + j·Q(t)
-fc
Euler: e-jφ = cos(φ) - j·sin(φ)
fs
f
fs-fd
complex-valued signal Z(t)
fc-fd
e-j...
fs/2
IZ(f)I
IZ[m]I
FFT-spectrum of the sampled radar-sensor output signal z[n] = I[n]+j·Q[n]
f
-fd
fs/2
FFT
fftshift
IZ[m]I

## Slide 9
Exercise 2
Assume that the target moves towards the radar sensor (v>0) and, thus, causes a positive Doppler frequency (fd>0)
In the following diagram, sketch the magnitude spectra
IY(f)I of the reflected radar signal y(t) and
IZ(f)I of the analog radar sensor output signal z(t) = I(t)+j·Q(t)
IZ[m]I of the sampled radar-sensor output signal z[n] = I[n]+jQ[n]
IY(f)I
fc
f
fc
f
fs/2
IZ(f)I
fs
f
IZ[m]I
f
fs/2
FFT
fftshift
IZ[m]I

## Slide 10
Use the Matlab-program CW_Doppler_Radar_8kSps_160.m, read the corresponding wave-file and determine the Doppler-frequency fd and the resulting radial (Doppler-) velocity v. The result should look like this:
Exercise 3
fs = 8 kSps
NFFT = 256
TFFT = N∙Ts = 32 ms
Δf = 1/TFFT = fs/N ≈ 31 Hz
detected fd = -156.3 Hz (instead of -160 Hz)
detected radial velocity v = -0.98 m/s (away from the radar, instead -1 m/s)
test also with NFFT = 64
direction of movement cannot be determined!
fd is negativ (movement away from the radar)

## Slide 11
Exercise 4
Use the Matlab-program CW_Doppler_Radar_4kSps_waveByhand.m read the corresponding wave-file and determine the resulting Doppler-velocity-profile v(t). The result should look like this:
the hand was moved first towards the sensor and then away from the sensor
signal level below threshold
fs = 4 kSps
NFFT = 256
TFFT = N∙Ts = 64 ms
Δf = 1/TFFT = fs/N ≈ 15.6 Hz

## Slide 12
DSP-Design-Scenario
Speed sensor: moving car, max. range 40-60 m (see below)
vmax = 80 km/h
Doppler frequency fd = ± 3556 Hz
sampling frequency fs = 8 kSps is larger than 2∙IfdI
block length N = 256
measurement time TFFT = N∙Ts = 32 ms (car moves < 0.7m during this time)
FFT frequency resolution Δf = 1/ TFFT ≈ 31 Hz (corresponds to 0.7 km/h)
accuracy of the speed indication is ±0.35 km/h

## Slide 13
Link Budget
4 dBm
Gantenna = 8 dB
Effective Isotropic Radiated Power
EIRP = 12 dBm
GLNA = 10 dB
Sensitivity
PRx ≥ -105 dBm (B=1kHz, S/N=6dB,...)
Pout
≥ -87 dBm
Radar Range Equation @ 24 GHz
R = 0.0167 · 10S/40 · σ0.25
(S in dB and σ in m2)
Round-trip loss S ≤ 117 dB = 12 - (-105) (Datasheet: overall sensitivity = -118 dBc)
Exercise 5: Compute the maximum (detection) range R of the CW-Doppler-Radar
for a moving person:
for a moving car:
Radar Cross Section
(σ ≈ 1 m2 for moving person σ ≈ 50 m2 for moving car)
Range R
Gantenna = 8 dB
K-LC5 data sheet

## Slide 14
Detection Range
K-LC5 data sheet
RCS

## Slide 15
Gain of external amplifier
Parameter | Value | Remarks
Sensitivity K-LC5 | -105 dBm | e.g. moving person @ a range of 14 m
receiver gain | 18 dB | see data sheet K-LC5
min. Pout | -87 dBm | @ R = 1 kΩ output of LNA
Pout in mW: 10·log10(Pout/1mW) ≥ -87 dBm => Pout ≥ 10-8.7 mW
Vout, rms in V: √(R*Pout) => Vout, rms ≥ 10-8.7/2 V = 45 μV => Vout ≥ 64 μV
But: the 12 Bit ADC has a dynamic range ≈ 3V, i.e. an LSB of 732 μV!
therefore, an external gain amplifier is required: VADC = Vout·Gamp
with Gamp = 60 dB, i.e. Gamp = 1000: VADC ≥ 64 mV, i.e. at least 6 LSBs
AC-coupling is required for such a (high) gain, but the high-pass-filter removes the low frequencies and, thus, the small v-values. There is a minimal detectable speed vmin > 0

## Slide 16
Parameter | Values | Remarks
EIRP | 12 dBm | effective isotropic radiated power
Round-trip-loss | dB | see slide 13, R = 3 m, RCS = 1 m2
received power PRx | dBm | see slide 13
receiver gain | dB | see slide 13
max. Pout | dBm | @ R = 1 kΩ output of LNA
max. Pout | mW | @ R = 1 kΩ output of LNA
max. Vout | mV | @ output of radar sensor
max. VADC | V | 60 dB external gain
Assumption: a moving person is in short distance (3m) directly in front of the sensor
Exercise 6:
Fill out the column «values» of the following table and verify, that a «large» received signal does not over-drive the ADC (no clipping).
Gain of external amplifier

## Slide 17
Radar-Sensor
K-LC5
Field-Of-View: 80°x34°
6 m
16.8 m (@ r=10m)
    Radar Sensor K-LC5 data sheet K-LC5
Overall S = 118 dBc (B=1kHz, S/N=6dB, ...)
Rmax moving person ≈ 15 m
Sensitivity: -105 dBm (B=1kHz, S/N=6dB,...)
Rx gain: 18 dB
FMCW supported
3.3V version ordered
(Digikey, K-LC5-RFB-00C, CHF 25.-/pcs)

## Slide 18
radar sensor K-LC5
3.3V power supply
amplifier (60 dB) for I- and Q-output highpass, VCO in (DAC)
test points LED?, switch?, buzzer?
filter analog 5V power supply
USB power supply
CW-Doppler-Radar: Hardware
a PCB-template is available
Sensor board
STM32F4-Discovery-Board
MCU board
Option: 3D-printed lens for focussing

## Slide 19
Subsystem Test Scenarios
1. Sensor-Board without radar sensor K-LC5 and without MCU-board
Function Generator (sin, 100 Hz…4 kHz, 50 μV…1 mV) at I-/Q-connector pins
validate the external amplifier outputs with the oscilloscope (in front of ADC)
check also the magnitude frequency response
2. Sensor-Board with radar sensor K-LC5 and without MCU-board
put the Radar Doppler Target K-DT1 in front of the radar sensor
validate the external amplifier outputs with the oscilloscope (in front of ADC)
3. MCU-Board with FFT-firmware and without radar sensor board
FuGe (sin, 100 Hz…4 kHz, 50 mV…1V, 1.5V DC-offset) at ADC inputs
show and validate frequency on the display