## Slide 1
Tobias Otto, „Principles of FMCW Radars“, TU Delft, see http://de.slideshare.net/tobiasotto/principle-of-fmcw-radars.
slides 1-7: principle of FMCW radar
slide 15: block diagram of an FMCW radar
slide 12: FMCW radar signal processing
Option FMCW-Radar
Classical RADARs are based on pulse-echo-technique
- distance determination by Time-of-Flight (ToF) measurement
- see https://de.wikipedia.org/wiki/Radar => „Impulsradar“ => animation
Disadvantages of pulse-echo-RADARs
- long radio range requires high power (short) Tx-pulses
- high range resolution requires very short-time pulses
One solution: FMCW-RADAR

## Slide 2
t
f
Bsweep e.g. 260 MHz
Tsweep e.g. 1 ms
Trep
tToF
Tsweep = NFFT·Ts
range R=?
FMCW-Radar: how it works
dynamic or static target
Time-of-Flight tToF = 2∙R/c
fbeat = s·tToF
Slope of frequency ramp s = Bsweep/Tsweep
detection of fbeat or tTOF or range R
modulation

## Slide 3
FMCW-Radar: frequency-difference fbeat ~ range R
  Exercise: find fbeat = …………………………………………………
  CW-Radar: frequency-difference fd ~ Doppler-velocity
Rx-signal is multiplied with Tx-signal inside sensor
  frequency-difference appears at the sensor-outputs e.g: I(t) = A·cos(2π·fbeat·t-φ0)
  detection of frequency difference fbeat with FFT of length NFFT
Range-resolution ∆R = c / (2∙Bsweep)
  e.g: Bsweep = 260 MHz => ∆R = 0.6 m
  Independent of ramp slope S and FFT-length NFFT
FMCW-Radar Parameters

## Slide 4
c = 299 792 458 m/s (speed of light)
Bsweep = 260 MHz (Bsweep is typically given)
Tsweep = 1 ms (choice)
Slope s = Bsweep / Tsweep = 260 MHz / 1 ms (indirect choice by Tsweep)
fs = 64kHz (choice) Range « / 2» since it is an echo and the measurement path has been travelled twice. Frequency resolution = 1kHz (= FFT resolution if Ts ∙ NFFT = Tsweep) Range resolution: 0.58m Max. Range:
 Rmax can be adjusted by adjusting Tsweep or fs
If Ts ∙ NFFT = Tsweep  Rmax =
FMCW-Radar Parameters

## Slide 5
Additional FMCW-HW-Requirements
DAC generates sawtooth-signal for VCO-input
  Anti-Imaging-filter: RC-TP 1. order (fg = 10 kHz) is sufficient
  VCO-Input voltage range: 0 bis 3.3 V
  VCO-Input impedance 20 kΩ
Sampling of sensor signal I(t) (and maybe Q(t))
  Support of fs up to 100 kHz
  Bandwidth of analog Gain-Amplifier up to 50 kHz Gain-Bandwidth-Product of PM4-OpAmp is 2 MHz => 2 amplifier stages are required!
start of f-ramp and FFT-block must be «synchronized»