## Slide 1
Meaning of «Micro-Doppler» (https://www.mathworks.com/help/phased/ug/introduction-to-micro-doppler-effects.html)
A moving target introduces a frequency shift in the radar return due to Doppler effect. However, because most targets are not rigid bodies, there are often other vibrations and rotations in different parts of the target in addition to the platform movement. For example, when a helicopter flies, its blades rotate, or when a person walks, their arms swing naturally. These micro scale movements produce additional Doppler shifts, referred to as micro-Doppler effects, which are useful in identifying target features.
Option Micro-Doppler-Evaluation
Some questions in CW-Radar signal processing
Can the steps of a person be detected in the radar signal?
Is a human / non-human presence detector realizable?
How fast rotate the blades of a fan / drone / …?

## Slide 2
Setup for Micro-Doppler Evaluation
Instruments-Inputs (not XLR!)
USB
5V
ASIO driver
Matlab (or Python)
sampling (audio) signals with fs = 48 kSps (or 44.1 kSps)
resampling to 4, 6, 8, 9.6, 12 or 16 kSps according need
record to wav-file & offline-computation of «spectrogram»
alternatively, online-computation (live-mode)
option: synch with video sequence
I(t)
Q(t)
Sensor-Board (without MCU-Board)
Notebook (or Smartphone)

## Slide 3
Results of a field test
Radar K-LC6, 60 dB Gain, USB-Audio-Interface
(fs = 4 kSps, NFFT = 256, hanning-window)
Jogging & arm swinging?
fast walking
Δv = 0.1 ms IvI > 0.2 ms
sw: -60…0 dBc